## Slide 1: Cyber-Physical Systems: modelling – linear and non-linear systems part 2
Workshop: March 16-18 (2023).
Erasmus+: Development of practically-oriented student-centred education
in the field of modelling of Cyber-Physical Systems (CybPhys)
Joan Peuteman

## Slide 2: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 3: Spring-mass-damper system
A spring-mass-damper system is a very typical example of a system which can be described by a second order linear differential equation.
A force is applied to
the mass implying a
displacement .
A spring has a spring constant
and notice the viscous friction
coefficient .
Based on the second law of Newton

## Slide 4: Spring-mass-damper system
By using a Laplace transform, a linear differential equation can be replaced by an algebraic equation. Solving such an algebraic equation is much easier. By taking the inverse Laplace transform, the solution of the original differential equation is obtained.
Pierre Simon de Laplace

## Slide 5: Spring-mass-damper system
Solving time-invariant differential equations using Laplace transforms.
original
differential equation
solution
difficult
Laplace transform
reformulation of the problem
algebraic equation
solution in the Laplace
domain
inverse
Laplace transform
the longer way around
using Laplace transforms
is often much easier

## Slide 6: Spring-mass-damper system
The Laplace transform can be written as
and the corresponding inverse Laplace transform can be written as

## Slide 7: Spring-mass-damper system
Let’s use Laplace transforms to solve the differential equation
describing the behaviour of the spring-mass-damper system. By taking the Laplace transform, an algebraic equation is obtained:
Assume no external force is applied. Moreover, the initial condition and
The solution in the Laplace domain

## Slide 8: Spring-mass-damper system
The solution in the Laplace domain
describes the spring-mass-damper system with an initial condition and no input force .
By taking the inverse Laplace transform
the behaviour of the spring-mass-damper system in the time-domain is obtained.

## Slide 9: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 10: Second order system
When considering a second order system, a distinction can be made between
an overdamped system,
a critically damped system,
an underdamped system.
The spring-mass-damper system is an example of such a second order system.
Important are the roots of the denominator
i.e. the poles:

## Slide 11: Second order system
An overdamped system is obtained in case i.e. the viscous damping coefficient is high.
In such a situation, both poles and are real valued and stricly negative.
The poles: the roots of the denominator.
A zero: root of the numerator
s-plane

## Slide 12: Second order system
We omit the calculations but by taking the inverse Laplace transform of
one obtains that
(overdamped system)

## Slide 13: Second order system
An overdamped system with e.g. , and implies an evolution of (with )
time
Due to friction without oscillations.
Quite slow evolution of to zero.

## Slide 14: Second order system
A critically damped system is obtained in case .
In such a situation, both poles and are real valued and stricly negative. Notice that
We omit the calculations, but by taking the inverse Laplace transform of
one obtains that

## Slide 15: Second order system
An critically damped system with e.g. , and implies an evolution of (with )
time
Due to friction .
goes to zero, this evolution is faster
compared to the overdamped system.

## Slide 16: Second order system
An underdamped system is obtained in case i.e. the viscous damping coefficient is low.
In such a situation, both poles and are complex with a stricly negative real part.
A zero: root of the numerator
The poles:
the roots of the denominator.
s-plane

## Slide 17: Second order system
We omit the calculations but by taking the inverse Laplace transform of
with
(underdamped system)
The poles can be written as

## Slide 18: Second order system
We omit the calculations but by taking the inverse Laplace transform of
one obtains that
(underdamped system)

## Slide 19: Second order system
An underdamped system with e.g. , and implies an evolution of (with )
time
Due to friction
Oscillations due to the underdamped behaviour.

## Slide 20: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 21: Two rolling vehicles
Consider two rolling vehicles.
Vehicle has a mass and position . Vehicle has a mass and position .
An external force is applied to vehicle .

## Slide 22: Two rolling vehicles
Notice the connection between both vehicles with spring constant and viscous damping coefficient .
Notice the connection between vehicle and a fixed wall with spring constant and viscous damping coefficient .

## Slide 23: Two rolling vehicles
The behaviour of vehicle needs consideration of all forces acting on this vehicle.
due to the spring
due to the damper
Based on the second law of Newton

## Slide 24: Two rolling vehicles
The behaviour of vehicle needs consideration of all forces acting on this vehicle.
Based on the second law of Newton
due to the spring
due to the spring
due to the damper
due to the damper

## Slide 25: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 26: State variable model
As an example, consider again the system with two rolling vehicles.
Instead of using the two second order differential equations obtained in the previous paragraph, it is possible to use four first order differential equations.

## Slide 27: State variable model
Defining four states , , and as
This allows to use four first order differential equations instead of two second order differential equations.

## Slide 28: State variable model
The second order differential equation
can be replaced by
The second order differential equation
can be replaced by

## Slide 29: State variable model
When using the state variable model (of linear time-invariant systems), generally the differential equations are written in the form
with appropriate matrices and . When contains states then is an matrix and is an matrix.
When considering the two rolling vehicles, and

## Slide 30: State variable model
When considering the two rolling vehicles, the general expression
equals

## Slide 31: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 32: State variable model: Laplace
When taking the Laplace transform of
one obtains that
By solving this set of algebraic equations, the solution in the Laplace domain equals
By taking the inverse Laplace transform, the solution in the time-domain equals

## Slide 33: State variable model: Laplace
As already stated, starting from
one obtains that
The matrix exponential function can be calculated as

## Slide 34: Table of content
Spring-mass-damper system
Second order system
Two rolling vehicles
State variable model
State variable model: Laplace
Two rolling vehicles: example

## Slide 35: Two rolling vehicles: example
Consider the system with two rolling vehicles.
MATLAB can be used to calculate the behaviour of the two
rolling vehicles.
In the present example, no external force has been applied.
The behaviour due to an initial condition has been calculated.

## Slide 36: Two rolling vehicles: example
The position of vehicle 1:
position
time
goes to zero as .

## Slide 37: Two rolling vehicles: example
The position of vehicle 1:
Initially, energy has been stored in
spring 1 with spring constant due
to initial condition .
Losses occur due to the dampers with damping coefficients and .
This leads to a damped oscillatory motion.
goes to zero as .

## Slide 38: Two rolling vehicles: example
The position of vehicle 2:
position
time
q goes to zero as .

## Slide 39: Two rolling vehicles: example
The position of vehicle 1:
Initially, energy has been stored in
spring 1 with spring constant due
to initial condition .
Losses occur due to the dampers with damping coefficients and .
This leads to a damped oscillatory motion.
q goes to zero as .
Initial condition

## Slide 40: Thank your for your attention! Questions?